## Slide 1: High-Speed Digital Field Visualization of Currents and Crosstalk
Yuriy Shlepnev – Simberian Inc.
Presented at Signal Integrity webinar on August 15, 2017

## Slide 2: Dr. Yuriy Shlepnev Simberian Inc.
Yuriy Shlepnev is President and Founder of Simberian Inc., where he develops Simbeor electromagnetic signal integrity software. He received M.S. degree in radio engineering from Novosibirsk State Technical University in 1983, and the Ph.D. degree in computational electromagnetics from Siberian State University of Telecommunications and Informatics in 1990. He was principal developer of electromagnetic simulator for Eagleware Corporation and leading developer of electromagnetic software for simulation of signal and power distribution networks at Mentor Graphics. The results of his research are published in multiple papers and conference proceedings.

## Slide 3: Outline
Introduction
Electromagnetic field visualization basics
Current crowding, skin-effect, power flow
Cross-talk microstrips and strips
Cross-talk in vias
Conclusion

## Slide 4: PCB/Packaging interconnects: multiport or black-box description
Port1
Port2
S-parameters
TDR/TDT
Eye Diagram
Compute and measure Multiport Parameters
Let’s take closer look at how we usually model it…

## Slide 5: Analysis – more “black boxes”
See more at Y. Shlepnev, “Decompositional Electromagnetic Analysis of Digital Interconnects”, IEEE Int. Symp. on Electromagnetic Compatibility (EMC2013), Denver, CO, 2013, p.563-568.
Transmission line segments (multiports)
Multiport Circuit (connection of multiports)
What is inside of those “black boxes”?
Discontinuities (multiports)
S-parameters
Modal & RLGC

## Slide 6: “Black box” contains fields
Looking at the S-parameters/TDR/TDT/eye we see just the tip of an ICEBERG!
What we do not usually see contains a lot of information that is almost never “measured”, but is critical to revealing “How interconnects work”
Electric and magnetic fields, current densities, power flow density…
[S]

## Slide 7: Fields are described by Maxwell’s equations
Gauss’s laws
Ampere’s law
Faraday’s law (Kirchhoff’s voltage law)
- Electric Intensity (V/m)
- Magnetic Intensity (A/m)
- Electric Flux (Coulomb/m^2)
- Magnetic Flux (Tesla or Weber/m^2)
- Free Charge Density (Coulomb/m^3)
- Free Current Density (A/m^2)
- Polarization (Coulomb/m^2)
- Magnetization (A/m)
Fields in materials
Plus material equations and boundary conditions….
Very complicated to say the least 
Visual Computational Electromagnetics may be helpful tool to understand…
Continuity (Kirchhoff’s current law)

## Slide 8: Field visualization in 19th century
Michael Faraday, Experimental Researches in Electricity, 1855
Faraday visualized fields with the iron fillings and almost never used equations;
He discovered and described electromagnetic induction (Faraday’s law) using words only;
That leaded to the discovery of the Maxwell’s equations…

## Slide 9: EM fields visualization – 70s & 80s
Use of printers:
Electric Field in rectangular waveguide T-junction
Print out from VOLNA software of B.V. Sestroretzkiy, V.M. Seredov, N.A. Sadovnikov, МНИИП (now Corporation Vega)
TE10 wave

## Slide 10: EM fields visualization – 70s & 80s
Electric fields in microstrip line on magnetized ferrite substrate computed with Minimal Autonomous Blocks (Treftz’s finite elements)
From В.В. Никольский, Т.И. Никольская, Декомпозиционный подход к задачам электродинамики, Наука, 1983, с. 176-181.

## Slide 11: EM fields visualization – 70s & 80s
IEEE Antennas and Propagation Society International Symposium, 1981, p. 634-637.
Far-field space-time contour plot for a Gaussian-pulse excitation of a center-fed dipole, 1981
Mostly use of plotters and printers until 90s …

## Slide 12: 90s and 2000s - gaming changed everything…
Personal computers and console video games took a great graphical leap forward in the 2000s, becoming able to display graphics in real time computing that had previously only been possible pre-rendered and/or on business-level hardware (https://en.wikipedia.org/wiki/Computer_graphics).
Surface current density and electric field in strip lines computed and visualized in Simbeor software

## Slide 13: Time and Frequency Domains
Signal -> Harmonics
Response -> superposition of distorted signal harmonics
t
t
Signal degradation in interconnects are caused by dielectric and conductor loss and dispersion, high-frequency non-TEM wave dispersion, effect of discontinuities (ISI or multiple reflection) and radiation;
The best way to model those effect is in the FREQUENCY DOMAIN (our focus);
All fields, currents and power are real parts of time-harmonic complex vectors
Excitation – single frequency sinusoidal voltage sources
period
frequency
[S]

## Slide 14: Time-harmonic vector fields
Instantaneous field value: amplitude and direction are periodic functions of time
Peak value:
Average value (for power flow):
are complex numbers

## Slide 15: Equations or Pictures
Which one do you understand?
Which one will you remember?
Plane wave solution
Richard Feynman: Dirac said that to understand a physical problem means to be able to see the answer without solving equations. Maybe he exaggerated; maybe solving equations is experience you need to gain understanding. But until you do understand, you're just solving equations. - 1979
wavelength
(animated)

## Slide 16: Field modeling technique: Trefftz Finite Elements
V.V. Nikol’skii, T.I. Lavrova, “The method of minimum autonomous blocks and its application to waveguide diffraction problems,” Radio Engineering & Electronic Physics, vol. 23, no. 2, p.1-10, 1978.
V.V. Nikol’skii, T.I. Nikol’skaia, Decompositional approach to electromagnetic problems. Moscow: Nauka, 1983 (in Russian).
Y.O. Shlepnev, Trefftz finite elements for electromagnetics. - IEEE Trans. on Microwave Theory and Techniques, vol. MTT-50, pp. 1328-1339, May, 2002.
Projection on boundaries
S-parameters of Trefftz element
Element interior fields (exact solution of Maxwell’s equations):
[S]
S-parameters of structure

## Slide 17: Fields and currents in strip line
Modal and RLGC(f) parameters are extracted from the analysis of small segment in Simbeor for analysis of traces with arbitrary length
1 V, 50 Ohm
50 Ohm
Strip 1.2 mil thick, 7 mil wide
~50 Ohm
Vpeak ~ 0.5 V
Ipeak ~ 0.01 A
Dk=3.76, LT = 0.006 @ 1 GHz
Planes 0.77 mil thick, 17.2 mil apart
1 V, 50 Ohm
50 Ohm
Example from demo-video #2016_03: How Interconnects Work™: EM field, current and power flow in strip line
-
+

## Slide 18: Electric Field at 1 GHz
Electric Field (V/m, peak values)
+
+
+
-
-
-
-
-
-
Voltage
Will integration path matter?
Is it transverse (TEM) wave?
Transverse components
Longitudinal component (small)
Hint: No longitudinal components only without losses in conductor and dielectric

## Slide 19: Magnetic Field at 1 GHz
Magnetic Field (A/m, peak values)
Currents
Displacement current (bound charges)
Conduction current (free charges)
Transverse components
Field inside conductor
Longitudinal component (small)

## Slide 20: Currents in Ampere’s law
V
-
+
electric field
current
- bulk conductivity, Siemens/m
Translational motion of free charges in electric field described by the Ohm’s law (LTI):
Conduction current (A/m^2)
+ + + + + + + + + +
- - - - - - - - - -
+ + + + +
- - - - -
V
electric field in vacuum
polarization
smaller electric field in dielectric
-
+
Polarization [Coulomb/m^2] is displacement of charges bound to atoms, molecules, lattices, boundaries,… described by material (constitutive) equations (LTI):
Displacement in vacuum and polarization currents
See more in the “Material World…” tutorial, DesignCon 2016 at www.simberian.com

## Slide 21: Current density in strip line: current crowding
f=0.1 MHz
sd=8.2 mil
t/sd=0.146
f=1 MHz
sd=2.59 mil
t/sd=0.46
Concentration of current below the strip at higher frequency
Almost uniform distribution through thickness, both in planes and strip
Strip width 7 mil, t=1.2 mil, planes 0.77 mil;
Peak values are shown; sd is skin depth;
Ir=-0.005 A
Is=0.01 A

## Slide 22: Current density in strip line: transition to skin-effect
Current flow in thin layer at 1 GHz (typical PCB)
f=10 MHz
sd=0.82 mil
t/sd=1.46
f=1 GHz
sd=0.082 mil
t/sd=14.6
Non-uniform current distribution - onset of the skin-effect in strip
Strip width 7 mil, t=1.2 mil, planes 0.77 mil;
Peak values are shown; sd is skin depth;

## Slide 23: Current density in strip line: well-developed skin-effect
f=10 GHz
sd=0.026 mil
t/sd=46.15
f=30 GHz
sd=0.015 mil
t/sd=80
Current flow in very thin layer of conductor, higher currents at the edges
Ir=-0.005 A
Is=0.01 A
Maximal currents are at the edges – the edge singularity at high frequencies
Strip width 7 mil, t=1.2 mil, planes 0.77 mil;
Peak values are shown; sd is skin depth;

## Slide 24: Skin depth and reversal of current
Poynting’s vector
y
Skin depth
Plane-wave solution inside conductor
Current density in strip at 10 MHz (sd = 0.82 mil)
Current density in strip at 1 GHz (sd = 0.082 mil)
(animated)

## Slide 25: Surface current density
Current density (A/m^2)
Surface current density (A/m)
Magnetic field intensity -> current in circuit theory

## Slide 26: Power flow density at 1 GHz
W/m^2
- circuit theory
Longitudinal component outside of conductors dominates
Poynting vector is energy passing through unit area in 1 sec

## Slide 27: Power flow in strip line
f=0.1 MHz
f=10 MHz
More power flows along the line closer to strip edges at higher frequency
Conductor absorbs power
Peak value of power flow density [W/m^2]
Conductor interior

## Slide 28: Power flow in strip line
f=10 MHz
sd=0.82 mil
t/sd=1.46
f=1 GHz
f=30 GHz
Power flow concentration near the strip edges continues as frequency rises
Conductor interior absorbs more power (30 GHz), scaled arrows in dB
Peak value of power flow density [W/m^2]
Energy passing through conductor boundary is absorbed by the conductor

## Slide 29: Cross-talk in microstrips
12-mil strips, 12 mil apart
1 V, 50 Ohm
50 Ohm, NEXT
50 Ohm, FEXT
50 Ohm, Through
NEXT: Near-End Crosstalk
FEXT: Far-End Crosstalk

## Slide 30: Power flow density in microstrips
5 GHz, wavelength ~1.5 in
25 GHz, wavelength ~0.3 in
50 GHz, wavelength ~0.15 in
Small FEXT
Half of power goes into FEXT
Almost all power goes into FEXT
What if segment length is 5 inch?
(animated)

## Slide 31: Power flow density in microstrip
25 GHz, wavelength ~0.3 in
Instantaneous at 20 ps

## Slide 32: Surface current density in microstrip
25 GHz, wavelength ~0.3 in
Instantaneous at 20 ps
Almost identical currents in opposite directions
Current is mostly on the aggressor line
See more at demo-video #2016_11: How Interconnects Work™: Crosstalk power flow in microstrip lines

## Slide 33: Power flow density at strip lines
See more at demo-video #2016_11: How Interconnects Work™: Crosstalk power flow in microstrip lines
25 GHz, wavelength ~0.3 in, Instantaneous at 0 ps
1 V, 50 Ohm
Very small NEXT
Very small FEXT
12-mil strips, 12 mil apart
Looks like nothing going on the victim trace?

## Slide 34: Surface current density in strip lines
1 V, 50 Ohm
25 GHz, wavelength ~0.3 in, Instantaneous at 0 ps
See more at demo-video #2016_11: How Interconnects Work™: Crosstalk power flow in microstrip lines
Hint: superposition of even and odd modes

## Slide 35: Cross-talk in differential vias
p1
p2
p3
p4
NEXT – S[D1,D3]
FEXT – S[D1,D4]
Two coupled differential vias in a 120 x 120 mil area caged with PEC wall
Vias are 30 mil apart, antipad 25x55 mil, traces 8 mil MSL, 8 mil separation;
The first cage resonance is at about 12 GHz (half wavelength in dielectric)
Stackup from CMP-28 board, Wild River Technology http://wildrivertech.com
See more at App Note #2013_06 at http://www.simberian.com/AppNotes.php
Three cases:
20 mil
40 mil
40 mil + 5 vias

## Slide 36: Power flow density in closely spaced differential vias
5 GHz
30 GHz
small NEXT
NEXT
FEXT
Differential excitation, half of the structure is shown
(animated)

## Slide 37: Power flow density in 40-mil separated differential vias
5 GHz
30 GHz
smaller NEXT
smaller FEXT
Differential excitation, half of the structure is shown
(animated)

## Slide 38: Power flow density in differential vias with stitching vias
5 GHz
30 GHz
no NEXT
Very small FEXT
Differential excitation, half of the structure is shown
(animated)

## Slide 39: Surface current density on planes and vias
Instantaneous current density at 30 GHz, t=2ps
TOP
BOTTOM

## Slide 40: More visualization at www.simberian.com...
#2017_02: How Interconnects Work™: Microstrip over meshed reference plane in flex interconnects, 16 min
#2016_13: How Interconnects Work™: Crosstalk power flow in differential vias, 10 min
#2016_12: How Interconnects Work™: Crosstalk power flow in single-ended vias, 11min
#2016_11: How Interconnects Work™: Crosstalk power flow in microstrip lines, 12min
#2016_10: How Interconnects Work™: Coaxial connector launch localization, 10 min
#2016_09: How Interconnects Work™: Power flow in coaxial connector launch, 16 min
#2016_08: How Interconnects Work™: EM fields, surface current and power flow in single-ended vias - with and without stubs, 15 min
#2016_07: How Interconnects Work™: Conductor roughness part 2 - modelling with Roughness Correction Coefficients, 16 min
#2016_06: How Interconnects Work™: EM fields and power flow in differential vias, 16 min
#2016_05: How Interconnects Work™: Currents and power flow in differential vias, 10 min
#2016_04: How Interconnects Work™: Conductor roughness modeling with Effective Roughness Dielectric, 10 min
#2016_03: How Interconnects Work™: EM field, current and power flow in strip line, 10 min
#2016_02: How Interconnects Work™: Skin-effect in microstrip line - current density, 10 min
#2016_01: How Interconnects Work™: Skin-effect in microstrip line - EM fields and current density, 17 min

## Slide 41: Conclusion
Usefulness of visualization
  Better understand or electromagnetics
  Better understanding of “How interconnects work”
  Troubleshooting problem setup and software
Simbeor electromagnetic signal integrity software (Simbeor THz version 2017.02) is used for all computations and visualization plots
See more at app notes and demo-videos of “How Interconnects Work” at http://www.simberian.com