## Slide 1: Welcome to
Santa Clara Convention Center
Conference
January 28 - 30, 2020
Expo
January 29 - 30, 2020

## Slide 2: Machine Learning Applications for COM Based Simulation of 112 Gb Systems
Alex Manukovsky, Intel alex.manukovsky@intel.com
Yuriy Shlepnev, Simberian Inc.
shlepnev@simberian.com
Zurab Khasidashvili, Intel
zurab.khasidashvili@intel.com
Eli Zalianski, Intel
eli.zalianski@intel.com
Santa Clara Convention Center
January 29, 12:00pm - 12:45pm, Ballroom F

## Slide 3: Outline
Introduction
ML Based Systematic Design Space Exploration
  Feature Range Analysis
  COM based interconnect system analysis
  Interconnect modeling and feature selection
ML Design Space Exploration Examples
Conclusion

## Slide 4: SerDes Design Challenge
100 Ports
15 Supported protocols
5 Physical Interfaces
How to approach the Design Complexity?

## Slide 5: Coverage challenge in SerDes design
Multiple usage models
  Compliance to multiple specifications
  Unique channel requirements for each protocol
  Unique requirements for each of the three test types
  Different physical interfaces support
Solution space coverage
  Cable lengths
  PCB trace length and topologies
  Connectors
  EQ capabilities
PCB manufacturing tolerances
PVT Variation
Solution space chart
Too many parameters and expertise-based analysis maybe not be sufficient - an automated systematic approach is required!

## Slide 6: Design Space Exploration In 4 Steps
  What are the important features that impact the system behavior the most?
  What are the ranges of each of the important features in which we are most likely to achieve desired system response?
  What are the combinations of feature ranges that enable us to achieve desired system response?
  What are the feature ranges where system is most likely to fail?
*System parameters are features in ML terminology
**SerDes system response is COM metric with 3 dB pass-fail
1
2
3
4
Expert Opinion
(SI Eng)
Generate link models covering the solution space
(1k-1M cases)
Analyze System performance for each case
(x10 cases)
Understand
the results
Define solution space
COM script
(Matlab)
3D EM Simulator
(Simbeor)
ML
(EVA tool)
Covering:
Design options
PCB Manufacturing variation
Covering:
PVT corners
EQ capabilities
Linc partners
OP modes

## Slide 7: Feature Range Analysis
Feature Range Analysis is ML technique designed to help answering those questions and automate the decision process

## Slide 8: Range Analysis
Feature Range Analysis identifies combinations of ranges of numeric (or continuous) features and levels of nominal (or categorical) features that explain positive samples – samples whose characteristics and the behavior we want to explore in the data (COM>3 or COM<3)
Algorithm resembling Rule Learning, Rule Induction, and Subgroup Discovery – see analysis and references in the paper
Z. Khasidashvili, A. J. Norman. Range Analysis and Applications to Root Causing. In: 6th IEEE International Conference on Data Science and Advanced Analytics, DSAA 2019.

## Slide 9: Range Analysis Algorithm
Ranks features highly correlated to the response with 2 procedures: Ranking procedure uses Ensemble Feature Selection (select most relevant features) Basis procedure uses Maximal Relevance Minimal Redundancy (MRMR) to select a subset of features which both strongly correlate to the response and provide a good coverage of the entire variability in the response
Apply ranking and basis procedures to select the most relevant single ranges of the selected features, and in addition select single ranges that maximize one or more quality functions
Generate range- combinations of features and apply ranking, basis and quality procedures to select the most relevant ranges for combinations of features
Implemented in Intel’s EVA software

## Slide 10: Range Analysis Quality Function
N – count of all samples; Pos – count of positive samples; p0=Pos/N
R – range; n(R) – count of all samples within that range;
True Positive Rate (aka sensitivity, recall, or hit rate): TPR(R) = TP(R)/Pos
where TP(R) denotes the count of true positive samples - positive samples within R;
Predictive Positive Value (also known as precision): PPV(R) = TP(R)/n(R);
The lift: Lift(R) = PPV(R)/p0 – likelihood to have more positive samples within R;
Weighted Relative Accuracy: WRAcc(R) = (n(R)/N)*(PPV(R)–p0)
Goal of design exploration with RA is to identify ranges R that maximize Lift(R), WRAcc, and/or other quality functions that are most suitable for the application at hand

## Slide 11: COM Based Interconnect System Analysis

## Slide 12: COM In Nutshell
DIE A
Package
PCB
DIE B
AC Caps
Stripline or Microstrip Link
Package
Peak Signal – includes all losses accounted in model and equalization
Peak SER Noise – includes losses, ISI, crosstalk and random noise with some assumptions and equalization
>3 dB for pass threshold
>4 dB for excellent links
Channel Operating Margin (COM) – single real number ideally for RA

## Slide 13
TP0
TP5
TP0-TP5
TPa
TPb
TPa
TPb
S-parameters computed or measured over sufficient bandwidth suitable for 112 Gbps PAM4 time domain conversion:
a) S-parameters of links with crosstalk from TP0 to TP5 if vendor or the reference package model is used;
b) S-parameters of links with crosstalk from TPa to TPb for analysis with package model;
2) COM script – Matlab script from IEEE P802.3ck group is used;
COM Base System Performance
What is needed to compute COM?

## Slide 14: Other inputs to COM
Transmitter (Tx)
  Voltage swing (Av)
  Nonlinearity (R_LM)
  Rise/Fall Time (Tr)
  Jitter (sigma_RJ and A_DD)
  Noise (SNR)
  FFE tap ranges plus limits (c(k))
Receiver (Rx)
  One-sided noise spectral density (eta_0)
  Bandwidth limiting filter (f_r)
  Reference CTLE (g_DC, f_z, f_p1, f_p2) and noise filter (g_DC_HP, f_HP_PZ)
  Number of ideal DFE taps plus limits (N_b, b_max(n))
  Detector error ratio (DER_0) related to forward error correction (FEC) choice
  Termination resistor (R_d)
H. Wu, M. Shimanouchi, M. P. Li, COM & IBIS-AMI How They Relate & Where They Diverge, DesignCon 2019
Most of the parameters are from the reference 802.03ck (C2C) script;
Equalization parameters are optimized by the reference script;
Number of DFE taps was 1 and 5;
Details and references in the paper…

## Slide 15: Interconnect System Modeling and Feature Selection
Major Signal Degradation Factors:
Thermal losses – dielectric and conductor effects
Reflections – characteristic impedance mismatch and discontinuities
Couplings - leaks and interference

## Slide 16: Extraction of channel S-parameters: 1D+3D decompositional approach
Tx
Tx Package (COM)
Rx
Rx Package (COM)
3D EM
3D EM
2D quasi-static
1D TLine

## Slide 17: Models to compute S-parameters of links
1D models or transmission line models – Telegrapher’s equations
Modal or per unit length parameters for the Telegrapher's equations (Z, Y) are computed with static or quasi-static field solver (2D problems for Laplace's equations) or an electromagnetic fields solver (3D problems for Maxwell's equations)
Lines with coupling, multimodal waveguides, periodic structures can be accurately modeled as 1D
3D models or 3D full-wave models - everything described and solved with Maxwell's equations without any simplifications for 3D geometries or field components
Analysis of discontinuities such as via-holes, connectors or any type of transitions between uniform traces
1D+3D: Hybrid de-compositional analysis with transmission line models for traces (1D) and 3D models for discontinuities or transitions (Y. Shlepnev, EMC 2013)
The best technique for the serial interconnects under the localization condition This approach usually works for PCB and packaging problems with a relatively long traces, but may fail if trace segments are too short – complete 3D analysis is required in this case

## Slide 18: Accuracy of 1D+3D de-compositional analysis
Accuracy depends on proper localization of every single element in the link
Broadband dielectric and conductor roughness models are identified (with GMS-parameters or SPP Light)
  Very important for PCB – models must be statistical for 56-112 Gbps (see more A. Manukovsky, Y. Shlepnev, DesignCon 2019, EPEPS 2019), about time to start doing it for packages
Manufactured geometry adjustments are identified or statistical models are available
Electromagnetic solvers are formally validated with measurements using systematic approach (“sink or swim” for instance)
  See more at M. Marin, Y. Shlepnev, DesignCon 2018, EMC 2018, Webinar #8
Other considerations: Ports consistency and de-embedding, boundary conditions,…

## Slide 19: Thermal losses: dielectric and conductor
6x1.2 mil strip in dielectric with Dk=4.2 (50 Ohm, typical size)
Ultra-Low loss (LT=0.001,Meg7)
Smooth copper
Copper with HVLP surface, SR=0.14 um, RF=8.7
Copper with STD/RTF surface, SR=0.4um, RF=2
Medium loss (LT=0.01, FR408)
Dielectric from ultra-low loss (LT=0.001) to medium loss (LT=0.01); Use causal Wideband Model (Djordjevic-Sarkar) defined with 2 parameters (Dk and LT) at one frequency point;
Conductor and conductor roughness: use causal Huray-Bracken models defined with 2 parameters (SR and RF) with previously identified values;

## Slide 20: Features affecting thermal losses and reflections due to impedance mismatch
Feature | Description
Ha | Height of dielectric layer above strips
Hb | Height of dielectric layer below strips
T | Strip thickness
W | Strip width in the middle of strip layer
S | Spacing between strips (middle)
EF | Strip etch factor – EF=0.5(Wtop-Wbot)/T
RR | Conductor resistivity relative to annealed copper
SR | Surface roughness in um for Huray-Bracken roughness model
RF | Surface roughness factor for Huray-Bracken roughness model
Dk | Dielectric constant at 1 GHz for Wideband Debye dielectric model
LT | Loss tangent at 1 GHz for Wideband Debye dielectric model
Length | Differential strip line length
1
2
3
4
Length
Stripline segment (PKG and PCB)
Select possible laminates – defines Ha, Hb, Dk, LT, RR, SR, fix EF;
Set S for strong or weak coupling; Compute W for about 10% and 5% deviation from Ztarget

## Slide 21: Reflections: PCB vias discontinuity
3D EM models (s4p): 3 cases
Reflection, dB
TDR, Ohm
Example of model building and optimization

## Slide 22: Features affecting coupling
2 coupled differential stripline or microstrip segments on PCB
Spp – diff. pair to pair separation
Lcp – length of coupled section
Stackup features - same as for differential pairs
Stripline or microstrip
Spp
Example of features for xtalk investigation from MLKit of Simbeor SDK
All other types of couplings (localization breakout, mode conversion, multipath propagation,…) are either mitigated by design or ignored in this investigation

## Slide 23: ML Design Exploration Examples 112 Gb Chip to Chip Link
1) Simple 112 Gbps PCB link case
2) Realistic 112 Gbps link with PCB discontinuities and crosstalk

## Slide 24: Simple 112 Gbps link case
 | Feature |  |  |  |  |  | 
1 | Tx_PCB_TL_S (S/H) | 1 | 2 | 3 |  |  | 
2 | Tx_PCB_TL_L (Length) [in] | 0.5 | 1 | 3 | 6 | 9 | 12
3a | PCB_Dk (Dk) | 2.8 | 3.2 | 3.5 | 3.8 |  | 
3b | PCB_LT (LT) | 0.001 | 0.002 | 0.004 | 0.009 |  | 
4 | PCB_TL_H (Ha,Hb) [mil] | 3 | 5 | 8 | 10 |  | 
5 | PCB_Imp, [Ohm] | 85 | 90 | 95 | 100 | 105 | 
6 | PKG_Len, [mm] | 1 | 5 | 12 | 31 |  | 
Insertion Losses (dB) for some PCB links
DOE Table: 5760 cases
+Reference package parameters, 1 tap DFE
Simulated with Simbeor SDK

## Slide 25: Simplest link RA results – long PKGs (12 and 31 mm)
Results of ranking and basis procedures: strongest correlation to response and variability (coverage)
Single-range features maximizing quality
Package length is highly rated by both procedures – this is the most important element of the link
Positive: COM>=4
Negative COM<4
  What are the important features that impact the system behavior the most?

## Slide 26: Simplest link– long PKGs (12 and 31 mm)
Positive: COM>=4
Negative COM<4
  What are the ranges of each of the important features in which we are most likely to achieve desired system response?
 | range_1 | score | selection | Positive Out | Negative Out | Positive In | Negative In | Range Lift
1 | 31:Inf | 1.0 | correlation-coverage-target | 0 | 4319 | 2251 | 2063 | 2.001159
 | range_1 | score | selection | Positive Out | Negative Out | Positive In | Negative In | Range Lift
1 | 6:6 | 0.2184 | target | 1630 | 5563 | 621 | 819 | 1.653923
2 | 6:9 | 0.2674 | target | 1129 | 4627 | 1122 | 1755 | 1.495682
3 | 3:9 | 0.3490 | correlation-coverage-target | 628 | 3688 | 1623 | 2694 | 1.441859
Pkg_len_RX
s4p_Tx_PCB_L

## Slide 27: Simple link: long packages (12 and 31 mm)
COM > 3dB
COM < 3dB
COM
Total Loss, dB
Total Loss, dB
COM
COM > 3dB
COM < 3dB
Blue: PKG_Len=12mm
Brown: PKG_Len=31mm
PCB Link Length
COM vs. Total Loss at Nyquist frequency – longer package is better
PKG 12mm
PKG 31mm
COM vs Loss for two package lengths
COM vs Loss for two package lengths and different PCB lengths
0
2
4
6
8
10
12
s4p_Tx_PCB_L

## Slide 28: Why 12mm Rx package is a Challenge
4in PCB link, IEEE 802.3ck reference package: Cd=120fF, Ls=120 pH Cb=30fF, Cp=90fF, Lp=12mm
SSR (Tsymb=17.8571ps, Trise=4ps)
4in PCB link, IEEE 802.3ck reference package: Cd=120fF, Ls=120 pH Cb=30fF, Cp=90fF, Lp=31mm
SSR (Tsymb=17.8571ps, Trise=4ps)
Reflections cause ISI
Shorter package (12mm)
Longer package (31mm)
Reflections cannot be mitigated with 1 tap DFE!

## Slide 29: Simple link– long PKGs (12 and 31 mm)
Important range-pair features
Positive: COM>=4
Negative COM<4
Important range triplet features
Combinations of features with package and PCB link length have highest lift – proper selection increases likelihood of success
  What are the combinations of feature that impact the system behavior the most? (enabling us to achieve desired system response)

## Slide 30: Simple link RA results – long PKGs
Positive: COM>=4
Negative COM<4
  What are the combinations of feature ranges that enable us to achieve desired system response? (maximizing quality )
 | s4p_PCB_Imp range_1 | s4p_Tx_PCB_L range_2 | Pkg_len_RX range_3 | score | selection | Positive Out | Negative Out | Positive In | Negative In | Range1 Lift | Range2 Lift | Range3 Lift | Triplet Lift
1 | -Inf:90 | 6:6 | 31:Inf | 0.3600 | target | 1963 | 6382 | 288 | 0 | 1.282095 | 1.653923 | 2.001159 | 3.835184
2 | -Inf:95 | 6:6 | 31:Inf | 0.4577 | target | 1822 | 6379 | 429 | 3 | 1.220420 | 1.653923 | 2.001159 | 3.808551
3 | -Inf:95 | 3:Inf | 31:Inf | 0.8263 | correlation-coverage | 888 | 6018 | 1363 | 364 | 1.220420 | 1.298165 | 2.001159 | 3.026842

## Slide 31: Simple link: PCB link length effect
COM > 3dB
COM < 3dB
Total Loss, dB
Blue: PKG_Len=12mm
Brown: PKG_Len=31mm
COM vs Loss for two package lengths and different PCB lengths (L)
COM
L=0.5in
L=1in
L=3in
L=6in
L=9in
L=12in
COM vs. Total Loss at Nyquist frequency -
Optimal link length is between 3 and 9 inches
PCB channel 6 inches along with 31mm package is the best option

## Slide 32: Simple link: PCB dielectric effect
COM > 3dB
COM < 3dB
Total Loss, dB
PKG_Len=12mm
PKG_Len=31mm
COM vs Loss for different dielectrics and PCB lengths
Dk=2.8
LT=0.001
Dk=3.2
LT=0.002
Dk=3.5
LT=0.004
Dk=3.8
LT=0.009
COM < 3dB
COM > 3dB
PCB Link Length
COM
COM vs. Total Loss at Nyquist frequency -
Better dielectrics improve link quality for longer links
However not in every case it is beneficial to go for low Dk option

## Slide 33: Simple link: dielectric thickness effect
COM > 3dB
COM < 3dB
Total Loss, dB
PKG_Len=12mm
PKG_Len=31mm
COM vs Loss for different diel. thickness and PCB lengths
H=3mil
COM < 3dB
COM > 3dB
PCB Link Length
COM
H=5mil
H=8mil
H=10mil
COM vs. Total Loss at Nyquist frequency
Thicker dielectrics improve link quality for longer links
However in links (below 9 in) thin dielectrics will provide similar performance
For short links (below 3 in) thin dielectric has an advantage

## Slide 34: Simple link– short PKGs (1 and 5 mm)
Single-range features
Triplet range features
PKG length is not important
Lift is small – most of the cases pass 4 dB threshold
Lets ask the opposite question
Positive: COM>=4
Negative COM<4
Positive: COM>=4
Negative COM<4
  What are the important features that impact the system behavior the most?

## Slide 35: Simple link – short PKGs (1 and 5 mm)
Single-range features
Important range triplet features
Ranking results are similar to the excellent system (COM>=4) for 12 and 31 mm PKGs case
High Lift scores
Positive: COM<3
Negative COM>=3
  What are the feature ranges where system is most likely to fail?

## Slide 36: Simple link: short packages
COM > 3dB
COM < 3dB
COM
Total Loss, dB
Total Loss, dB
COM
COM > 3dB
COM < 3dB
Blue: PKG_Len=1mm
Brown: PKG_Len=5mm
PCB Link Length
COM vs. Total Loss at Nyquist frequency – shorter package is better
PKG 5mm
PKG 1mm
COM vs Loss for two package lengths
COM vs Loss for two package lengths and different PCB lengths

## Slide 37: Realistic PCB link with crosstalk and discontinuities
 | Feature |  |  |  |  |  | 
1 | Tx_PCB_TL_S (S/H) | 1 | 2 | 3 |  |  | 
2 | Tx_PCB_TL_L (Length) [in] | 0.5 | 1 | 3 | 6 | 9 | 12
3a | PCB_Dk | 2.8 | 3.2 | 3.5 | 3.8 |  | 
3b | PCB_LT | 0.001 | 0.002 | 0.004 | 0.009 |  | 
5 | PCB_TL_H (Ha, Hb) [mil] | 3 | 5 | 8 | 10 |  | 
6 | PCB_Imp [Ohm] | 85 | 90 | 95 | 100 | 105 | 
7 | Tx_PCB_TL_DS (Spp) [mil] | 3 | 5 | 10 |  |  | 
8 | SR [um] | 0.075 | 0 |  |  |  | 
9 | PKG_Len [mm] | 5 | 12 | 31 |  |  | 
0.8*Length
0.2*Length
Optimized discontinuities + reference package model
DOE Table: 25920 cases
Simulated with Simbeor SDK

## Slide 38: Realistic link S-parameters
Insertion Loss, dB
Reflection, dB

## Slide 39: Realistic link with xtalk and 1 DFE tap
 | feature_1 | score | selection
1 | Tx_PCB_DS | 1.0000 | correlation-coverage
2 | PCB_H | 0.6766 | correlation-coverage
3 | PCB_Imp | 0.1452 | correlation-coverage
4 | Tx_PCB_L | 0.1392 | correlation-coverage
5 | PCB_Dk | 0.0839 | correlation
6 | PCB_LT | 0.0839 | coverage
7 | Pkg_len_TX | 0.0508 | coverage
8 | PCB_SR | 0.0418 | coverage
9 | Tx_PCB_S | 0.0025 | coverage
Most relevant features
Important single range features
Positive: COM>=3; Negative COM<3

## Slide 40: Important single range features
Differential pair to pair separation single range
Dielectric thickness – two possible single ranges
Positive: COM>=3; Negative COM<3
Proper selection of differential pair to pair separation and dielectric thickness increases likelihood of success

## Slide 41: Realistic link crosstalk
FEXT, dB
NEXT, dB

## Slide 42: Important range-pair features
Pair ranges for differential pair to pair separation and dielectric thickness
The most important pairs, high Lift
Positive: COM>=3; Negative COM<3

## Slide 43: Dielectric thickness and pair to pair separation effect
COM > 3dB
COM < 3dB
COM, dB
Total Loss, dB
COM, dB

## Slide 44: Important range triplets features
Triplet ranges for dielectric thickness, package length and pair to pair separation.
The most important triplets
Triplet ranges for dielectric thickness, PCB link length and pair to pair separation.
Positive: COM>=3; Negative COM<3

## Slide 45: Realistic link with xtalk and 5 DFE taps
Important single range features
Excellent
Compliant
Package length is not so important with more taps!

## Slide 46: Realistic link with xtalk and 5 DFE taps
Important range triplets features
Excellent
Compliant
Package length is not even in the triplets for COM > 3dB!

## Slide 47: Conclusion
Practical application of a ML based method to identify the parameters with the greatest effect on 112 Gbps system response is demonstrated
Initial set of features (length, thickness, dielectric,…) is identified with some knowledge about the features contributing to signal degradation
The rest of the process is a completely automated design exploration with the ML algorithms – no expert knowledge is required
It can be used as a decision support tool for system architect, Si designer, SI Engineer,…

## Slide 49: Backup slides

## Slide 50: Couplings: Leaks and Interference
Coupling type | Model
Crosstalk – leaks and interference in parallel traces | INCLUDE
Via localization breakout – leaks and interference and through parallel planes and between vias | Localize vias up to 40-50 GHz and do not simulate via coupling
Couplings through slots and cutouts in reference planes | Prohibit in layout
Modal transformations in diff. pairs (aka skew) – bends, asymmetry in routing, FWE | Mitigate with proper length compensation – do not simulate
Multipath propagation, radiation, EMI, EMC,… | Suppress with localization – do not simulate

## Slide 51: Chip-to-Chip (C2C) de-composition
Tx
Tx PKG
Bumps
Balls
PCB
Rx PKG
Rx
AC Caps
PCB Vias
PCB Vias
BGA-PCB Vias
BGA-PCB Vias
Rx PKG line segment
Rx PKG line segment
PCB coupled line segment
PCB coupled line segment

## Slide 52: Simplest link: impedance effect
COM > 3dB
COM < 3dB
COM
Total Loss, dB
Total Loss, dB
COM
COM > 3dB
COM < 3dB
PKG 12mm
PKG 31mm
ERL
COM vs. Total Loss at Nyquist frequency – lower impedance is better
PKG 12mm
PKG 31mm
PCB Imp
COM vs Loss for two package length and different PCB impedances
COM vs Loss for two package lengths and different ERLs